## Slide 1: CENG2400 Revision Q1a
A system has an ARM processor with a 32-bit General Purpose Input Output (GPIO) module. Two on/off switches are connected to bit-3 and bit-5 (inputs) of the GPIO. If two switches are both on, set the bit-4 (output) of the GPIO to 1, otherwise set it to 0. Other bits are don’t care. The pins of the processor are already set to GPIO mode by default after power up.
  Draw the circuit for interfacing the switches to the GPIO inputs.

## Slide 2: Q1b
The following lines are included in a header file arm.h:
/* General Purpose Input/Output (GPIO) */
#define IO0PIN (*((volatile unsigned long *) 0xE0028000))
// read inputs of GPIO bits
#define IO0SET (*((volatile unsigned long *) 0xE0028004))
// set GPIO bits register
#define IO0DIR (*((volatile unsigned long *) 0xE0028008))
//set GPIO direction , 0=in,1=out
#define IO0CLR (*((volatile unsigned long *) 0xE002800C))
// clear GPIO bit register
Write a C language program segment for this system.

## Slide 3: Q2
(a) Discuss how each of the following programming systems is supported by an ARM microcontroller. Describe the registers used and give at least one application for each one.
  Stack,
  System calls,
  Subroutine calls.
(b) Discuss the operations of an external interrupt of a microcontroller.

## Slide 4: Q3
A signal S is shown below
You are given a microcontroller (e.g. ARM7) system which is running at 3.3 Volts. The system has a timer running at 1 KHz and timer interrupt is available.
  The system is used to measure the timing widths (T1, T2) of the pulses, roughly depicted in the above diagram. And save their values (in ms) into integer variables X1, X2 for T1, T2 respectively.
    Discuss the circuit to interface this signal to the microcontroller system.
    Draw the hardware system block diagram. Discuss the peripheral devices involved and the input/output methods you use for measuring T1 and T2.
    Write the pseudo code of your program.
T1
T2
Time=0
Voltage
5V
Time
10
Seconds
Signal S

## Slide 5: Q4
Referring to program X, fill in the blanks.
Location | N,Z,C,V | R0 | R1 | R2 | R3 | 
Just after LOC1 |  |  |  |  |  | 
Just after LOC2 (the first time LOC2 is executed) |  |  |  |  |  | 
Just after LOC2 (the last time LOC2 is executed) |  |  |  |  |  | 
Just after LOC3 |  |  |  |  |  | 
Bit N (negative), Z (zero), C (carry), V (overflow) are the bits in the status register CPSR.
List 12 addresses and their data
contents from “store2” (data is in
little endian format in this machine).

## Slide 6: Q4
;----- program X (in ARM assembly language) begins -------------------------
AREA |.data|, DATA, READWRITE ; RAM data memory address is starting at 0x40000000
store2 DCD 0,0,0
align;-------------------------------------------------------------
AREA |.text|, CODE, READONLY ;
EXPORT __main
__main
MOV R0,#0
MOV R1,#0
MOV R2,#0
MOV R3,#0
LDR R0,=store2
LDR R1,=0x00030007
STR R1,[R0]
STR R1,[R0,#8]
LOC1 MOV R0,#0
MOV R2,#0x08
MOV R3,#0
LOC2 ADD R3,#2
CMP R2,R3
LOC3 BNE LOC2
NOP ; no operation
END;----- program ends-------------------------

## Slide 7: Q5A
Referring to program P shown below, list the values of the items of
  Flag Z of cpsr.
  Registers r0, r1, r2, r3, r15.
  List the four addresses and their contents in hexadecimal format of the four address locations that hold the value of data1. (List each address and its content individually.)
At each of the following execution stages. . The processor is using the little-endian data format.
  After the execution of the statement labelled “loc1”.
  After the execution of the first and second times of the statement labelled “loop”.
  At “exit”.

## Slide 8: Q5B
;----- program P begins-------
AREA |.data|, DATA, READWRITE
; RAM data memory address is starting at 0x4000 0000
foo DCD 0,0
data1 DCD 0,0
align;----------------------------
; User Initial Stack & Heap
AREA |.text|, CODE, READONLY ;
EXPORT __main
__main mov r0,#0 ;
mov r1,#0; ;-this is at 0x0000 0110
mov r2,#0
mov r3,#0
loc1 mov r0,#2
ldr r1,=data1
ldr r2,[r1]
ldr r3,=0x12345678
loop add r3,#1
str r3,[r1]
subs r0,#1
BNE loop
exit
END;-----

## Slide 9: Q6
Some registers of an ARM processor and their values are shown below.
r13=0x4013 2300
r14=0x0000 9100
r15=0x0084 1180
r0=0x0000 0000
r1=0x0000 0001
r2=0x0000 0002
r3=0x0000 0003
Then, an instruction “STMEDr13!, {r0-r2,r14} “ is executed. After that is complete.
List the values of r0,r1,r2,r3 and r13,r14,r15 .
List the addresses and data (in hexadecimal) stored in the data memory locations that have been changed by the instruction.
Write down the instruction that can restore the values back to r0,r1,r2 and r14.

## Slide 10: Q7
An embedded system has a General-Purpose-Input-Output (GPIO) peripheral device. The GPIO port has 32 bits, P31,P30,..,Pi,..,P1,P0. An LED is attached to bit 0 of the GPIO, and an on/off switch is connected to bit 31 of the GPIO. The other GPIO bits are inputs and used for other purposes. The LED requires 30mA to run and has 2 Volts potential drop across its terminals. The output current of the GPIO bit is 10mA. The power supply provided is 3.3Volts.
The C-language functions for using the GPIO ports are:
Setup_direction_gpio(gpio_dir); /* gpio_dir is a 32-bit variable, if bit i of gpio_dir is 1, Pi is an output bit; otherwise it is an input bit.*/
set_gpio( gpio_set); /* gpio_set is a 32-bit variable. If bit i of gpio_clear is 1, Pi of GPIO is set. If bit i of gpio_set is 0, it has no effect. */
clear_gpio( gpio_clear); /* gpio_clear is a 32-bit variable. If bit i of gpio_clear is 1, Pi of GPIO is cleared. If bit i of gpio_clear is 0, it has no effect. */
val_gpio = read_gpio( ); /* val_gpio is a 32-bit variable. After this function is executed, the current status of the GPIO will be saved into val_gpio. */

## Slide 11: Q7 (continue)
setup_timer_interrupt_1KHz(); /* setup the timer interrupt at 1000Hz. The name of the timer interrupt service routine is “void timer_isr( )”;
  Draw the interface circuit for interfacing the LED and the switch to the embedded system.
  Write the pseudo code (based on the above C functions) of the system of the following different cases. Provide details of what parameters should be passed to the above C functions.
    After reset, when the switch is on, the LED is turned on, otherwise it is turned off.
    After reset, the LED is flashing at a regular frequency: turning on for one second and then off for one second precisely.

## Slide 12: Q8
A universal asynchronous receiver/transmitter (UART) of an embedded system (running on a polling input/output mode, not interrupt mode) has the following registers.
Status_reg (8-bit) :
- If the transmitter is empty, bit4=1, otherwise this bit is 0.
- If a valid data is received, bit7=1, otherwise this bit is 0.
- The other bits are not used here.
Send_buffer (8-bit) :
- It is used for holding the data byte to be sent.
Recieve_buffer (8-bit) :
- It is used for holding the data byte that has been received.
  Write the pseudo code of a C-language function “sendbyte (schar);” that sends a char variable “schar” to the serial output.
  Write the pseudo code of a C-language function “rchar=getbyte ( );” that receives a char variable “rchar” from the serial input.
  Write the pseudo code of a C-language function “sendhex ( hexbyte);” that sends the two ASCII presentation bytes of the 8-bit hexadecimal number hexbyte to the serial output. Hints: ASCII code for 0, is 0x30, 3 is 0x33, A is 0x41, B is 0x42 etc. For example if hexbyte is 0x2B, you send 0x32 and 0x42 to the serial port).
  Discuss why the polling input/output mode is not efficient. Explain how the interrupt mode can be used to make input/output more efficient.