## Slide 1: CENG3430 Tutorial 1
Introduction to Vivado

## Slide 2: Vivado
Programming using IDE for VHDL / Verilog
Download the compiled code to FPGA board

## Slide 3: Step 1: Start the software
Double click the Vivado icon in the desktop
Or start from the Start Menu

## Slide 4: Step 2: Create a new project
Or Click File -> New Project…

## Slide 5
Step 3 : Click Next

## Slide 6
Step 4: Enter the project name
Select the project location for storage

## Slide 7
Step 5: Select RTL Project -> Next

## Slide 8
Step 6:
1. Select Target language and simulator language as “VHDL”
2. Click “Create File”
Make sure the File type is VHDL
Give name to the source file
Click OK
3. Click Next
1
2
↑3

## Slide 9
Step 7: Click Next

## Slide 10
Step 8: Click Add Files, select the downloaded XDC file
Press Next or Press Next if no XDC file

## Slide 11
Step 9: Click Boards -> Select Zedboard -> Click Next

## Slide 12
Step 10: Click Finish

## Slide 13
Step 10: If you see this box, just click OK

## Slide 14: Now we can start writing our code
This is the programming interface :
Select different tools
Shows the IDE status / warning / error message
Source directory
Code writing area

## Slide 15
In the source directory, you will see the source file created in Step 6.
Double click to open it.
(It is normal to see the file name appears twice in syntax error files and non-module file if the source code is empty or has syntax error)

## Slide 16
Copy the code downloaded file eLearning

## Slide 17
After saving the code, the source directory should look like this

## Slide 18: How to write a testbench?
After finishing your source code
Under the source window, right click on the simulation sources
-> Add sources

## Slide 19
Select “Add or Create Simulation Sources” -> Next

## Slide 20
Click “Create File” -> Get the testbench a name
(Usually same name with your source code, adding _test as postfix)
-> “OK”->”Finish”
1.
2
3
4

## Slide 21
If you see this window, just click OK

## Slide 22: Generating testbench file
In Vivado, the testbench file will not generate automatically
(But the older software can do that… )
Go to http://vhdl.lapinoo.net/
Paste your main board source code on it, the website will generate the testbench file for you
Copy the generated content, replace all content in the Vivado testbench file

## Slide 23
Unfortunately, the generated content have to modify before we execute…
Remove those line
“end tb;” change to “end;”
Change the name, to match the name of testbench if you like
<-Add your test case here
For example :
A <= '0';
EN0 <= '0';
wait for 100 ns;
A <= '1';
EN1 <= '0';
wait for 100 ns;
Which means you force a constant 0 to A / EN0 for 100ns
After that, you force a constant 1 to A / 0 to EN0 for 100ns
This must be the entity name of the design you are trying to test. You first turn it into a component and test it

## Slide 24: Now you can run simulation
Flow Navigator->Run Simulation->Run Behavioral Simulation
May need to drag the signal (left side under Objects) names to the waveform window
Click this
To zoom in to the appropriate waveform window

## Slide 25: Now you can see the result
To adjust the width, modify tbPeriod in the testbench

## Slide 26: Exercise
Please follow the instructions to create a VHDL project
Create a new project and a source file
Implement an AND gate using VHDL in source file
Write an test bench file and add to the project
Run the simulation
Demo your simulation result to the tutor

## Slide 27: example
----------------------testing code ----------------------------------------
-- Company:
-- Engineer:
--
-- Create Date: 01/16/2017 09:15:55 PM
-- Design Name:
-- Module Name: test1 - Behavioral
-- Project Name:
-- Target Devices:
-- Tool Versions:
-- Description:
--
-- Dependencies:
--
-- Revision:
-- Revision 0.01 - File Created
-- Additional Comments:
--
----------------------------------------------------------------------------------
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
-- Uncomment the following library declaration if using
-- arithmetic functions with Signed or Unsigned values
--use IEEE.NUMERIC_STD.ALL;
-- Uncomment the following library declaration if instantiating
-- any Xilinx leaf cells in this code.
--library UNISIM;
--use UNISIM.VComponents.all;
entity test1 is
Port ( A : in STD_LOGIC;
B : in STD_LOGIC;
C : in STD_LOGIC;
F : out STD_LOGIC);
end test1;
architecture Behavioral of test1 is
begin
F<= (A nor B) and C;
end Behavioral;
--Test bench, may be generated by
--http://vhdl.lapinoo.net/testb
library ieee;
use ieee.std_logic_1164.all;
entity tb_test1 is
end tb_test1;
architecture tb of tb_test1 is
component test1
– this component name “test1” must be the same as the entity name I
--in the source you are trying to test
port (A : in std_logic;
B : in std_logic;
C : in std_logic;
F : out std_logic);
end component;
signal A : std_logic;
signal B : std_logic;
signal C : std_logic;
signal F : std_logic;
constant TbPeriod : time := 100 ns; -- EDIT put right period here
signal TbClock : std_logic := '0';
begin
dut : test1
port map (A => A,
B => B,
C => C,
F => F);
TbClock <= not TbClock after TbPeriod/2;
-- EDIT: Replace YOURCLOCKSIGNAL below by the name of your clock
-- YOURCLOCKSIGNAL <= TbClock;
stimuli : process
begin
-- EDIT , give cases for each testing poeriod, can add as many as you like
A <= '0';
B <= '1';
C <= '1';
wait for 100 ns;
A <= '0';
B <= '0';
C <= '1';
wait for 100 ns;
end process;
end tb;
ench/
Add
this
By
you
Change the Tbperiod time to a suitable range
Change the name to match the entity name (e.g. test1 here) of the design to be tested.

## Slide 28: Click the blue-arrow (T) to see the simulation